## Slide 1: Summits On The Air
Mountain Top Activations and Amateur Radio
Presented by:
Scott Bastian- AK6Q
Catalina Island

## Slide 2: Summits on the Air
How did it start?
What is it?
How do I participate?
Can I get any awards?
How do I start activating and what equipment should I use?
Safety and Operating

## Slide 3: "For as long as there has been radio, amateurs have taken their stations to the tops of mountains It’s perhaps a little surprising that no formal program for activating summits existed until March 2002!”
Halleakala, HI

## Slide 4: How did SOTA start?
Original idea of John, G3WGV
Developed with Richard, G3CWI
Launched on March 2nd 2002
Internet based activity
  Industrial strength database
    Over 2 million QSO's in SOTA Database
    Thousands of registered users
  Sophisticated web portal
  Alerting, spotting, forum, etc
  55 participating countries and over 60,000 peaks in the SOTA database and growing fast

## Slide 5: Summits on the Air
How did it start?
What is it?
How do I participate?
Can I get any awards?
How do I start activating and what equipment should I use?
Safety and Operating

## Slide 6: What is the SOTA program?
"Summits on the Air (SOTA) is an award program for radio amateurs and shortwave
listeners that encourages portable operation in mountainous areas. SOTA has been carefully
designed to make participation possible for everyone - this is not just for mountaineers!
There are awards for Activators (those who
ascend to the summits) and Chasers ( those who either operate from home, mobile or even on another Peak (S2S)
From www.sota.org.uk

## Slide 7: Scott AK6Q, Paul AC5S, Randy K0TNG, Rocky WB5NJU , Snowshoe Peak near Creed

## Slide 8: General SOTA Principles
Two ways to participate
  Activator
  Chaser
Points and Award System
1805 SOTA summits in Colorado
A wide variety of difficulty and elevation
  From 5324 feet to 14,443 feet
SOTA activation requirements:
  summit MUST be on the SOTA list
  Activation Zone (AZ) is within 25m (82 ft) of the summit
  equipment must be carried (no minimum distance)
  portable power no fossil fuel generators or vehicle power

## Slide 9: When is a peak not a SOTA peak?
Peak qualification rules:
  Prominence must be greater than 500 ft/150m from surrounding peaks
  (333 ft/100m for Oklahoma)
  Peaks may be on private or government property
    Private property with permission only
    NO TRESSPASSING
    Respect for Native American and Government properties
    (Not all qualified peaks are in the database new ones are added as managers update/grow the data base)

## Slide 11: Selected SOTA Associations
Some of the US Associations
W0C - USA Colorado
W0D - USA Dakotas
K0M- USA Minnesota
W5O - USA Oklahoma
W7A - USA Arizona
W7M - USA Montana
W7Y - USA Wyoming
W7I- USA Idaho
W7W -USA Washington
As of Apr 2011

## Slide 12: SOTA Scoring
Based on ASL elevation of a qualified peak
  Points Varies by Association
  Same principles for Chasers and SWLs
  May include a "seasonal bonus" for activators
  Colorado has a 3pt bonus for Dec 1- Mar 31 (>9k)
  Scoring for W0C Colorado: 1805 Peaks
Under 8000' | 1 point | 
8000' to <9000' | 2 points | 
9000' to <10,500' | 4 points | 
10,500' to <12,500' | 6 points | 
12,500' to <13,500' | 8 points | 
13,500' + | 10 points | 
Notes: Min. height for bonus 9000 ft Bonus period dates 1 December to 31 March inclusive Association sponsored awards No Association Awards at this time Association Manager Matt Schnizer - K0MOS k0mos@schnizer.com

## Slide 13
W0C Peaks in database
.

## Slide 14: Summits on the Air
How did it start?
What is it?
How do I participate?
Can I get any awards?
How do I start activating and what equipment should I use?
Safety and Operating

## Slide 15: Participation Roles
Activators - those who "activate" a peak
  Need 4 QSO any band to get points
Chasers - those who work the activator
  Need only the one QSO to get points
Short Wave Listeners - those who can confirm a QSO get same points
Notes: Any license class can participate….. 2 of our Colorado Mountain Goats have done VHF/UHF only for 1,000 points!

## Slide 16: Mt Crested Butte

## Slide 17: Web Tools for SOTA
www.sota.org.uk
  The main site about the SOTA program
www.sotawatch.org
  Alerts, spots, map, and a forum
  Register to participate
https://www.sotadata.org.uk/en/
Log QSO’s both Activator and Chaser
  Register to enter QSO's and see more detail
  WØC SOTA (wØc-sota.org)
  Lots of Colorado SOTA information
Notes: Will talk more on these tools/links

## Slide 18: Summits on the Air
How did it start?
What is it?
How do I participate?
Can I get any awards?
How do I start activating and what equipment should I use?
Safety and Operating

## Slide 19: Activator Roll of Honor

## Slide 20: SOTA Awards
Mountain Goat
  1000 activating points
Shack Sloth
  1000 chasing points
SWL
Association awards
Further certificates at 2500, 5000, 10000 points
Certificates
100, 250 and 500 points

## Slide 21: Summits on the Air
How did it start?
What is it?
How do I participate?
Can I get any awards?
How do I start activating and what equipment should I use?
Safety and Operating

## Slide 22: Bands and Modes
VHF and UHF
  A lot of 2m FM 146.580mhz
  SSB is popular
  CW is also used occasionally
HF
  A lot of CW, due to use of QRP equipment
- 10118 kHz, 14060 kHz, 14285kHz are
Popular watering holes
Sunset Pk Paul W6PNG

## Slide 23: Principal Rules for Activators
Cannot use motorized transport to summit
  but you can drive up close to it
Must operate from portable power source
Must carry all equipment to summit
Must make at least four QSOs
  Any mode, any band
QSO's via repeaters don't count
  Exception is via satellite

## Slide 24: Typical SOTA Equipment
Any HT is good… but you need more antenna
Yaesu FT817 and FT818
Elecraft KX2 and KX3
It's all a lot easier these days!
Equipment is smaller, lighter and more efficient
Battery technology has improved immensely

## Slide 25: Typical SOTA Antennas
HF (Dipole, EFHW, OCFD)
& Fiberglass Pole / string for throwing in a tree
VHF/UHF Arrow Yaggi / Log Periodic

## Slide 26
HF or VHF/UHF?
Take Your Pick, Or Do Both
VHF/UHF
  Height Above Average Terrain
  Basic/compact equipment: Handheld Transceiver (HT)
  Dependent on local chasers
  FM most common, SSB for VHF contests
  Technician Licensees can play!!!
HF
  Classic QRP operating (CW and SSB)
  Longer distance contacts
  More radio contacts
  Recommended: General License Class or higher
  (unless on CW)

## Slide 27: How Far Will My Signal Go on VHF?
Optical horizon from Pikes Peak: 120 miles, plus 15% for radio horizon = 138 miles
Mt Sunflower (highest spot in Kansas) is easily worked on 2m FM from Pikes Peak (160 miles)
Best DX between two 14er summits on 2m FM (Colorado 14er Event):
  Andy AAØCM on Longs Peak to Jan W3GEY on Sunshine Peak (188 miles)
Best 2m FM DX during Colorado 14er Event: Phil NØKE on Mt Bross to Larry NØLL near Smith Center, KS (375 miles)
Bob Witte, KØNR

## Slide 28: No Rubber Duck Antennas
A rubber duck antenna is the world’s most convenient crappy antenna.
BAD
Bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad bad
Bob Witte, KØNR

## Slide 29: Arrow II VHF/UHF Yagi Antenna
Bob KØNR
Mt Sneffels
Crossed Yagi Design
Two antenna connections, or use duplexer
2m gain= 5.9 dBd
70cm gain= 8.2 dBd
(2009 CSVHFS)

## Slide 30: Elk Log Periodic Antenna UHF/VHF
Scott ACØFQ
San Luis Peak
One feedline connection for 2m & 70 cm
Same polarization on both bands
2m gain= 6.6 dBd
70cm gain= 7.0 dBd
(Mfg datasheet)

## Slide 31: HF Operations Frequently get to be the pile up! Lots of DX Opportunities
Radios
Antennas
Mt Orizaba Catalina Island

## Slide 32: HF Radios
Small is GOOD
Light Batteries
Built in ATU
Low current RX
Multi mode
Small
No ATU
High Current RX
Affordable
Multi mode
CW only
No ATU
Very small and Light!

## Slide 33: HF Antennas and poles
Steve WGoAT

## Slide 34: Tech on the go!
Cell Phone Apps!
  iPhone
    SotaGoat
    Pocket SOTA
    Hamlog/Pignology
    HAMRS logging
    Android
    Pocket SOTA
    SOTA Finder
    HAMRS logging

## Slide 35: One of my Favorite apps!

## Slide 36: Summits on the Air
How did it start?
What is it?
How do I participate?
Can I get any awards?
How do I start activating and what equipment should I use?
Safety and Operating

## Slide 37: Mountain Safety
Weather /Lightning
Getting Lost
Gravity
Temperature
Rescue can be hours OR days away
Warning: Climbing mountains is inherently a dangerous activity. Do not attempt this without proper training, equipment and preparation.
AK6Q in previous assignment

## Slide 38: So now what…..How do I start?
PREP
Chose a peak of interest ( close to a destination maybe?)
Look up data from SOTA apps (SOTA Goat)
Plan a route (GAIA GPS app and desktop)
Weather check for day of activation
Verify your equipment: Radios, Batteries, antenna, logging
SAFETY GEAR, Weather Gear, Map, Compass, GPS, Cell/HT Batts, Food, Water, Clothes, Poles, Bivy?
Create an alert for the activation (SOTA Goat)

## Slide 39: Some at home resources
www.SOTAMAPS.org
Identify peaks
Plan trip and routes
Gives peak info
www.GAIAgps.com
Links to phone app with routes, maps driving directions…

## Slide 40: ACTIVATION DAY
Verify you have your gear in pack
Know your route and timing
Watch the weather, and enjoy the journey!
Set up on summit
Spot if possible Cell, APRS…. Ask a contact to spot you!
Log your QSO’s
  Paper Log or notes (pencil?)
  HAMRS…… (ADIF)

## Slide 41: Signal Butte Summer Trip

## Slide 42: Now what to do with that log?
  Use SOTA Data Base for tracking
    www.sotadata.org.uk/en/
    Paper Logs scan be manually entered
    Import an ADIF File

## Slide 43: Squaw Peak (Mestaa`ehehe)

## Slide 44: Lets do SOTA!
You don't have to be a mountaineer!
  Some summits you can drive near the top
  You can participate as a Chaser from your shack
But if you are...
  There are many first expeditions yet to be done
  It's a good excuse to enjoy the outdoors on the summit looking at the views
  It's a great way to bring two hobbies together
  Be careful it is ADDICTIVE!!!

## Slide 45: Maybe Just Chase ???
Is it the points/awards? ...Bragging rights?
Fine tuning and keeping your station/
antenna in peaked performance?
Respect? Payback for being chased?

## Slide 46: Why Chase Responses
Larry K0RS:
Chasing QRP stations with improvised antennas...frequently on another continent...is a real DX challenge. Pulling a weak signal from the noise teaches one how to get the most from one's radio as well as fundamentals of propagation. And a dose of patience as well. The problem is, SOTA is addicting.
Paula K9IR:
When you chase summit activators, you can:
Join over 6,300 other hams in the chase, nearly 4,000 of them also activate summits.
Enjoy making contacts and qualifying for awards without needing a super-station.
Improve your ability to tune in, hear and work weak signal stations.
Help activators log the required minimum 4 QSOs

## Slide 47: Chaser Tools
www.SOTALIVE.tk

## Slide 48: Questions?
www.sota.org.uk
www.sotawatch.org
http://groups.yahoo.com/
WØC SOTA (w0c-sota.org)